# Mendel90 Instructions

The build is broken down into sub assemblies that can be worked on sequentially by one person, or in parallel if there is more than one person building. For this reason each assembly begins on a new page so the instructions can be separated.

15-11-12 First release of this manual.
25-11-12 Made Z cable 100mm longer. Added advice about temperatures.
03-12-12 Fixed missing Z parts. Added Skienforge and bed sections.
30-11-12 Z bar clamps and Y bearing mounts no longer have separate switch versions.
21-12-12 T2.5 belt and pulleys, new extruder PCB and Jhead mount.
02-01-13 Minor corrections and suggestions from users.
03-03-13 Removed feed tube connector.
14-03-13 Updates from user feed back and latest part renders.
21-03-13 Added section on using other software.
20-05-13 Added warning about absolute extrusion.
12-09-13 New X ends, Z couplers and fan bracket.
18-09-13 New file locations, SF profile, etc.
01-10-13 Updated remaining assembly views for black screws and red silicone on hot end.
18-11-13 Added instruction to fit nut and grub screw to extruder gear.
12-01-14 Fixed erroneous reference to hex screws in X motor assembly.
17-01-14 Added requirement for Philips screwdriver for removing X and E motor screws.
  Fixed erroneous z_min instead of z_max.
17-01-14 Clarified changing E_STEPS_PER_MM expression.
27-07-14 Small corrections and clarifications.
07-09-14 Fixed a few typos.
14-10-14 Fixed more typos.
12-03-15 Added bed cooling fan wiring details.
08-06-15 Changed belts and pulleys to GT2
--------------------------------------------
02-08-16 Changed by tvrrug.co.uk to have all wires run on top of the base. This makes the wire runs as short as possible and makes the chances of wires getting caught less.
02-08-16 Changed by tvrrug.co.uk to use the Prusa I3 X carriage system but with the X motor still on the right.
02-08-16 Changed by tvrrug.co.uk to use the Mk42 Bed.
02-08-16 Changed by tvrrug.co.uk to not use cable clamps. They are replaced with silicone/rubber wires held in place with zipties at each end

Table of Contents

1.General Build Tips	6
Tools Required	8
Recommended	8
Consumables	8
2.Frame Assembly	9
Vitamins	9
Printed parts	9
Assembly	10
3.Bed Fan Assembly	13
Vitamins	13
Printed part	13
Assembly	13
4.X Idler Assembly	15
Vitamins	15
Printed	15
Assembly	16
5.X Motor Assembly	17
Vitamins	17
Printed parts	17
Assembly	18
6.Z Motor Assemblies	23
Vitamins	23
Printed parts	23
Assembly	24
7.Z Axis Assembly	26
Vitamins	26
Printed parts	26
Sub-assemblies	26
Assembly	27
8.Y idler assembly	29
Vitamins	29
Printed parts	29
Assembly	29
9.Y motor assembly	30
Vitamins	30
Printed parts	30
Assembly	31
10.Y Carriage Assembly	32
Vitamins	32
Printed parts	32
Assembly	33
11.Y Heatshield Assembly	34
Vitamins	34
Assembly	34
12.Print bed assembly	35
Vitamins	35
Sub-assemblies	35
Bed Wiring	36
Assembly	38
13.Y Axis Assembly	39
Vitamins	39
Printed parts	39
Sub-assemblies	39
Assembly	40
14.X Carriage Fan Assembly	42
Vitamins	42
Printed parts	42
Assembly	42
15.X Carriage Assembly	43
Vitamins	43
Printed parts	43
Assembly	44
16.Hot end assembly	45
Vitamins	45
Assembly	45
17.Extruder connection PCB assembly	47
Vitamins	47
 Assembly	47
18.Extruder Motor Assembly	48
Vitamins	48
Printed parts	48
Sub-assemblies	48
Assembly	49
19.Extruder Assembly	51
Vitamins	51
Printed parts	51
Sub-assemblies	51
Assembly	52
20.X Axis Assembly	55
Vitamins	55
Sub-assemblies	55
Assembly	56
21.Spool holder assembly	58
Vitamins	58
Printed parts	58
Assembly	59
22.PSU assembly	60
Vitamins	60
Printed parts	60
Wiring	61
Summary	62
Assembly	63
23.Electronics Assembly	64
Vitamins	64
Printed Parts	64
Assembly	64
24.Software	68
Marlin Firmware	68
Arduino IDE	68
Pronterface	68
25.Testing	70
Jumpers	70
Power up	70
Limit switches	70
Motors	70
Heaters	71
Fan	71
26.Calibration	72
Bed Levelling	72
Extruder Calibration	73
Z Home Point	73
First Print	74
Slicing with Skeinforge	75
Extrusion Limits	76
27.Operating Instructions	77
Heated Bed	77
Changing filament	77
Removal	77
Insertion	78
Different types of filament	78
Cleaning the hobbed bolt	79
Using Other Software Tools	80